## Slide 1
CONTROL THEORY REVIEW: PID CONTROLLER
PID controller algorithm: proportional (P), integral (I) and derivative (D)
  P: depends on the present error
  I: accumulation of past errors
  D: prediction of future errors, based on current rate of change
The weighted sum is used to adjust the process via a control element (control valve)

## Slide 2
Consider a unity feedback system
e: error signal
r: desired input value
The PID controller in a transfer function form:
CONTROL THEORY REVIEW: PID CONTROLLERS
http://ctms.engin.umich.edu/CTMS/index.php?example=Introduction&section=ControlPID

## Slide 3
CONTROL THEORY REVIEW: SYSTEM PERFORMANCE PARAMETERS
Percentage overshoot measures how close the system response to the desired response.
Settling time is the time required for the system to settle within a certain percentage of the input amplitude.
For second order systems, desired response remains within 2-3% of the final value.

## Slide 4
: reduces the rise time and the steady state error but will never eliminates the steady-state error.
: eliminates the steady-state error for a constant or step input
: increases the stability of the system and reduces the overshoot
CONTROL THEORY REVIEW: PID CONTROLLERS IMPACT ON SYSTEM RESPONSE
http://ctms.engin.umich.edu/CTMS/index.php?example=Introduction&section=ControlPID